## Slide 1: 2st model
3-Floors elevator
with one manually-actuated door

## Slide 2: 3-Floors elevator
In this section, we model a three-floor elevator.
The additional complexities compared to the two-floor case are:
On the middle floor, the elevator is allowed to both descend and ascend.
It is necessary to introduce a button panel indicating to the elevator at which floor it should stop.
Note that in all the automata considered, the alphabet is composed only of the events present in the corresponding automaton.

## Slide 3: 3-Floors elevator
The following components are then modeled:
The sensor that detects the position of the elevator.
The elevator motor.
The button panel.
Note: The door open/close sensor is not modeled here because it is simpler to initially focus on these three components. This sensor will be implemented later.

## Slide 4: 3-Floors elevator
FIRST STEP: OUTLINE THE SYSTEM COMPONENTS
SENSORS:
FLOOR PRESENCE SENSORS:
Each floor is endowed with a presence sensor
BUTTON PANEL:
Inside the elevator cabin, a button panel is used to select the destination.
At each floor, a button can be used to call the elevator.
It is assumed that it is impossible to select a new button until the elevator has reached the desired floor selected by the last command.
ACTUATORS:
ELEVATOR MOTOR:
The motor can move the elevator up and down
F3
F2
up
down
F1

## Slide 5: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Position - floor presence sensors
F3
F2
up
down
F1
F2
to2
to1
F3
to2
to3
F1
The notations are the same as in the two-floor case, only the number of states of the automaton changes, as there are now three floors.

## Slide 6: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Button panel
up
down
For this automaton, are used three states, one for each button.
Events that influence the states of these:
: in the button panel the button that allows to reach the j-th floor is selected, when the cabin is at the i-th floor.
F2
F3
F1
s32
B1
B2
B3
s13
s31
s23
s21
s12

## Slide 7: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Motor – Elevator motor
F3
F2
up
down
Open / Closed
Events that influence the states of this model:
: the motor starts to lift the cabin
: the motor starts to lower the cabin
up_off : the motor stops to lift the cabin
down_off : the motor stops to lower the cabin
still_down: the motor continue to lower the cabin
still_up: the motor continue to lift the cabin
F1
Down
Off
downON
downOFF
Up
upON
upOFF
still_down
still_up

## Slide 8: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
F3
F2
up
down
Open / Closed
still_down: the motor continue to lower the cabin
still_up: the motor continue to lift the cabin
F1
Down
Off
downON
downOFF
Up
upON
upOFF
still_down
still_up
The addition of these two events is necessary when the elevator has to pass through more than one floor consecutively.
They allow us to obtain controllability of the overall system.

## Slide 9: 3-Floors elevator
There are two different types of behaviours to be enforced.
The physical constraints: 
The elevator cannot go any lower than floor 1 or any higher than floor 3
Elevator must go up (down) if the motor is working upwards (downwards)
Button panel can receive a new command only when the previous one has been executed
The desired behaviour:
For each button panel command:
The motor must start and stop once
The elevator must reach the desired floor and then stop
THIRD STEP: MODELING OF THE COMPONENTS

## Slide 10: 3-Floors elevator
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s start by working on automata of the components.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 11: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
The elevator cannot go any lower than floor 1 or any higher than floor 3
F1
F2
to2
to1
F3
to2
to3
upON
upON
downON
downON
PositionSensors

## Slide 12: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go up (down) if the motor is working upwards (downwards)
It is not enough to model the physical constraint when the elevator is on the second floor, since it can go up and down. It’s necessary to add specific constraints.
Down
Off
downON
downOFF
Up
upON
upOFF
to1
to2
to3
to2
Elevator motor
still_down
still_up

## Slide 13: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go up if the motor is working upwards
UpConstraint
NoUp
Rise
upON
upOFF
F2
upOFF
to2
F3
to2
upOFF
to3
to3
F3.5
still_up

## Slide 14: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go down if the motor is working downwards
NoDown
Lower
downON
downOFF
F2
downOFF
to2
F1
to2
downOFF
to1
to3
F1.5
still_down
DownConstraint

## Slide 15: 3-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Button panel can receive a new command only when the previous one has been executed
Constraint1command
Listening
Busy
s12
s13
s21
s23
s31
s32
upOFF
downOFF

## Slide 16: 3-Floors elevator
Else
GoF1
s21
s31
to1
upON
downOFF
FOURTH STEP: SPECIFICATION PHASE
For each button panel command, the elevator must reach the desired floor and then stop – boundary floor
Spa1

## Slide 17: 3-Floors elevator
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the elevator must reach the desired floor and then stop – case of an intermediate floor
Off
GoF2
s12
s32
to2
upOFF
downOFF
On
upOFF
downOFF
still_down
still_up
Spa2

## Slide 18: 3-Floors elevator
Else
GoF3
s13
s23
to3
upOFF
downON
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the elevator must reach the desired floor and then stop – boundary floor
Spa3

## Slide 19: 3-Floors elevator
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the motor must start and stop once
Off
Go
s12
s13
s21
s23
s31
s32
downON
upON
upOFF
downOFF
On
Spa4

## Slide 20: 3-Floors elevator
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s analyze the synchronous compositions.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 21: 3-Floors elevator
Position || Motor
Physical constraint
F1 | Down
F1 | Off
to2
to1
F2 | Down
F1 | Up
F2 | Off
F2 | Up
to2
to1
to2
to1
downON
downON
downOFF
downOFF
upOFF
upOFF
upON
upON
to3
to2
F3 | Down
F3 | Off
F3 | Up
to3
to2
to3
to2
downON
downOFF
upOFF
upON
still_up
still_up
still_up
still_down
still_down
still_down

## Slide 22: 3-Floors elevator
Phc1
F1 | Off
F1 | Down
to1
F2 | Down
F1 | Up
F2 | Off
F2 | Up
to2
downON
downOFF
downOFF
upOFF
upON
upON
to2
F3 | Down
F3 | Off
F3 | Up
to3
downON
upOFF
still_up
still_down
F2 | Down
F2 | StillUp
F2 | StillDown
to1
F2 | Up
to3

## Slide 23: 3-Floors elevator
Phc1
F1 | Off
F1 | Down
to1
F2 | Down
F1 | Up
F2 | Off
F2 | Up
to2
downON
downOFF
downOFF
upOFF
upON
upON
to2
F3 | Down
F3 | Off
F3 | Up
to3
downON
upOFF
still_up
still_down
F2 | Down
F2 | StillUp
F2 | StillDown
to1
F2 | Up
to3
These states have been added to represent the choice of stopping at the second floor or continuing to the next.

## Slide 24: 3-Floors elevator
Button Panel || Motor
Down | B1
Off | B1
Up | B1
Down | B2
Off | B2
Up | B2
Down | B3
Off | B3
Up | B3
upON
upOFF
upON
upOFF
upON
upOFF
downOFF
downON
downOFF
downON
downOFF
downON
s12
s21
s12
s21
s12
s21
s32
s23
s32
s23
s32
s23
s13
s31
s13
s31
s13
s31
Physical constraint
still_up
still_up
still_up
still_down
still_down
still_down

## Slide 25: 3-Floors elevator
Phc2 Button Panel || Motor
Down | B1
Off | B1
Up | B1
Down | B2
Off | B2
Up | B2
Down | B3
Off | B3
Up | B3
upON
upOFF
upON
upOFF
upON
upOFF
downOFF
downON
downOFF
downON
downOFF
downON
s12
s21
s32
s23
s13
s31
still_up
still_up
still_up
still_down
still_down
still_down
Refined automaton:

## Slide 26: 3-Floors elevator
Down | B1
Off | B1
Up | B1
Down | B2
Off | B2
Up | B2
Down | B3
Off | B3
Up | B3
upON
upOFF
upON
upOFF
upON
upOFF
downOFF
downON
downOFF
downON
downOFF
downON
s12
s21
s32
s23
s13
s31
Unwanted behaviour
still_up
still_up
still_up
still_down
still_down
still_down
Button Panel || Motor
s21
s23
s13
s31
s12
s32
s21
s23
s13
s31
s12
s32

## Slide 27: 3-Floors elevator
Down | B1
Off | B1
Up | B1
Down | B2
Off | B2
Up | B2
Down | B3
Off | B3
Up | B3
upON
upOFF
upON
upOFF
downOFF
downON
downOFF
downON
s12
s21
s32
s23
s13
s31
still_up
still_down
Sp2 Button Panel || Motor
s21
s23
s13
s31
s12
s32
s21
s23
s13
s31
s12
s32
Refined automaton:

## Slide 28: 3-Floors elevator
Pch2 || Sp2
Down | B1
Off | B1
Down | B2
Off | B2
Up | B2
Off | B3
Up | B3
upON
upOFF
upON
upOFF
downOFF
downON
downOFF
downON
s12
s21
s32
s23
s13
s31
Refined automaton:
still_up
still_down

## Slide 29: 3-Floors elevator
Button Panel || Position
F1 | B1
F2 | B1
F3 | B1
F1 | B2
F2 | B2
F3 | B2
F1 | B3
F2 | B3
F3 | B3
to2
to3
to2
to3
to1
to2
to1
to2
s12
s21
s12
s21
s12
s21
s32
s23
s32
s23
s23
s13
s31
s13
s31
s13
s31
to2
to3
to2
to1
s32
Physical constraint

## Slide 30: 3-Floors elevator
Phc3 Button Panel || Position
F1 | B1
F2 | B1
F3 | B1
F1 | B2
F2 | B2
F3 | B2
F1 | B3
F2 | B3
F3 | B3
to2
to3
to2
to3
to1
to2
to1
to2
s21
s12
s32
s23
s31
s13
to2
to3
to2
to1
Refined automaton:

## Slide 31: 3-Floors elevator
F1 | B1
F2 | B1
F3 | B1
F1 | B2
F2 | B2
F3 | B2
F1 | B3
F2 | B3
F3 | B3
to2
to3
to2
to3
to1
to2
to1
to2
s21
s12
s32
s23
s31
s13
to2
to3
to2
to1
Unwanted behaviour
s31
s21
s23
s13
s31
s12
s32
s21
s23
s13
s12
s32
Button Panel || Position

## Slide 32: 3-Floors elevator
F1 | B1
F2 | B1
F3 | B1
F1 | B2
F2 | B2
F3 | B2
F1 | B3
F2 | B3
F3 | B3
to2
to2
to3
to1
to2
to2
s21
s12
s32
s23
s31
s13
s31
s21
s23
s13
s31
s12
s32
s21
s23
s13
s12
s32
Sp3 Button Panel || Position
Refined automaton:

## Slide 33: 3-Floors elevator
Pch3 || Sp3
F1 | B1
F2 | B1
F3 | B1
F1 | B2
F2 | B2
F3 | B2
F1 | B3
F2 | B3
F3 | B3
to2
to2
to3
to1
to2
to2
s21
s12
s32
s23
s31
s13
Refined automaton:

## Slide 34: 3-Floors elevator
In the obtained automata, there are still undesired behaviors.
Through the synchronous composition of the models in pairs, it is not possible to eliminate the unwanted events.
A more adequate explanation is provided in the following slides.
Therefore, it is necessary to study the synchronous composition of all three models of our system.

## Slide 35: 3-Floors elevator
Phc1
F1 | Off
F1 | Down
to1
F2 | Down
F1 | Up
F2 | Off
F2 | Up
to2
downON
downOFF
downOFF
upOFF
upON
upON
to2
F3 | Down
F3 | Off
F3 | Up
to3
downON
upOFF
still_up
still_down
F2 | Down
F2 | StillUp
F2 | StillDown
to1
F2 | Up
to3
For example, we do not want the motor to activate immediately after it has turned off.

## Slide 36: 3-Floors elevator
Phc1
F1 | Off
F1 | Down
to1
F2 | Down
F1 | Up
F2 | Off
F2 | Up
to2
downON
downOFF
downOFF
upOFF
upON
upON
to2
F3 | Down
F3 | Off
F3 | Up
to3
downON
upOFF
still_up
still_down
F2 | Down
F2 | StillUp
F2 | StillDown
to1
F2 | Up
to3
For example, we do not want the motor to activate immediately after it has turned off.

## Slide 37: 3-Floors elevator
Phc1 || Phc2 || Sp2 || Phc3 || Sp3
Off_F1_B1
Off_F1_B2
Off_F1_B3
Up_F1_B2
Up_F1_B3
Up_F2_B2
Off_F2_B2
Up_F3_B3
Off_F3_B3
Off_F2_B1
Up_F2_B3
Off_F3_B2
Down_F3_B2
Down_F2_B2
Off_F2_B3
Down_F2_B1
Off_F3_B1
Down_F3_B1
Down_F1_B1
s12
upON
to2
upOFF
s13
upON
to2
still_up
to3
upON
upOFF
s32
downON
to2
downOFF
s31
downON
to2
still_down
to1
downOFF
s23
s21
downON
Down_F2_B1
Up_F2_B3
upOFF
upON
downON
downOFF
Unwanted behaviour

## Slide 38: 3-Floors elevator
TotalSystem1 Ph1 || PhSp2 || Ph3 || Sp3
Off_F1_B1
Off_F1_B2
Off_F1_B3
Up_F1_B2
Up_F1_B3
Up_F2_B2
Off_F2_B2
Up_F3_B3
Off_F3_B3
Off_F2_B1
Up_F2_B3
Off_F3_B2
Down_F3_B2
Down_F2_B2
Off_F2_B3
Down_F2_B1
Off_F3_B1
Down_F3_B1
Down_F1_B1
s12
upON
to2
upOFF
s13
upON
to2
still_up
to3
upON
upOFF
s32
downON
to2
downOFF
s31
downON
to2
still_down
to1
downOFF
s23
s21
downON
Down_F2_B1
Up_F2_B3
Refined automaton:

## Slide 39: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Doors can be open only if the elevator motor is off.
Elevator motor can turn on only if the doors are close.
The model of the 3-floors elevator must be integrated with the door motor.
The desired behaviour:

## Slide 40: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Let's consider a simple model, a manually-actuated door.
Closed
Open
open
close
F2
F1
up
down
Open / Closed
F1
The transitions will be triggered by the
proximity sensors of the cabin doors.
Events that influence the states of this model:
: the doors have been opened
: the doors have been closed
Doors

## Slide 41: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s start by working on automata of the components.

## Slide 42: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Doors can be open only if the elevator motor is off.
Elevator motor
Down
Off
downON
downOFF
Up
upON
upOFF
to1
to2
to3
to2
open
still_down
still_up

## Slide 43: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Elevator motor can turn on only if the doors are close.
Doors
Closed
Open
open
close
upON
downON

## Slide 44: 3-Floors elevator
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s analyze the synchronous compositions.

## Slide 45: Realistic door model
ElevatorMotor || Doors
Unwanted behaviour
Closed | Down
Closed | Off
open
close
Open | Down
Closed | Up
Open | Off
Open | Up
open
close
open
close
downON
downON
downOFF
downOFF
upOFF
upOFF
upON
upON
still_down
still_down
still_up
still_up

## Slide 46: Realistic door model
Sp4 ElevatorMotor || Doors
Closed | Down
Closed | Off
Closed | Up
Open | Off
open
close
downON
downOFF
upOFF
upON
still_down
still_up
Refined automaton:

## Slide 47: 3-Floors elevator
TotalSystem1 Ph1 || PhSp2 || Ph3 || Sp3
Off_F1_B1
Off_F1_B2
Off_F1_B3
Up_F1_B2
Up_F1_B3
Up_F2_B2
Off_F2_B2
Up_F3_B3
Off_F3_B3
Off_F2_B1
Up_F2_B3
Off_F3_B2
Down_F3_B2
Down_F2_B2
Off_F2_B3
Down_F2_B1
Off_F3_B1
Down_F3_B1
Down_F1_B1
s12
upON
to2
upOFF
s13
upON
to2
still_up
to3
upON
upOFF
s32
downON
to2
downOFF
s31
downON
to2
still_down
to1
downOFF
s23
s21
downON
Down_F2_B1
Up_F2_B3
Let's zoom in on these three states to see how the doors interact with the rest of the system.

## Slide 48: 3-Floors elevator
TotalSystem TotalSystem1 || Sp4
Off_F1_B1_Closed
Off_F1_B2_Closed
Off_F1_B3_Closed
s12
upON
s13
upON
downOFF
Off_F1_B1_Open
Off_F1_B2_Open
Off_F1_B3_Open
open
close
close
open
open
close
s12
s13
The same behavior is observed when the elevator is on the second and third floors, but always with the motor off.

## Slide 49: 3rd model
N-Floors elevator

## Slide 50: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
This model is a direct extension of the 3-Floors elevator, using the same components. “Motor” and “Door” automata remain unchanged:
Closed
Open
open
Door
close
Motor
Down
Off
downON
downOFF
Up
upON
upOFF
still_down
still_up

## Slide 51: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
“Position” and “Button panel” automata are modified as follows:
Position
F1
F2
to2
to1
F3
to3
to2
F4
to4
to3
F5
to5
to4
to6
to5
Button panel
B1
B5
B2
B3
B4

## Slide 52: N-Floors elevator
Due to the growing size of the automata, the case of a N-floor elevator will be treated using only one method.
Working directly on automata modeling single components
.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 53: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
The elevator cannot go any lower than floor 1 or any higher than the last floor
PositionSensors
F1
F2
to2
to1
F3
to3
to2
F4
to4
to3
to5
to4
Last
upON
downON
upON
downON
upON
downON
upON
downON

## Slide 54: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go up (down) if the motor is working upwards (downwards)
It is not enough to model the physical constraint when the elevator is at the intermediate floor, since it can go up and down. It’s necessary to add specific constraints.
Down
Off
downON
downOFF
Up
upON
upOFF
to1
to2
…
to(Last-1)
to3
to2
…
toLast
Elevator motor
still_down
still_up
open

## Slide 55: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go up if the motor is working upwards
UpConstraint
NoUp
Rise
upON
upOFF
F2
upOFF
to2
to3
…
to(Last-1)
F3
to2
upOFF
to3
to3
FLast
toLast
upOFF
F3
still_up

## Slide 56: N-Floors elevator
THIRD STEP: MODELING OF THE COMPONENTS
Elevator must go up if the motor is working upwards
DownConstraint
NoDown
Lower
downON
downOFF
FL-1
FL-2
to(Last-2)
F1
to1
downOFF
to2
to3
…
to(Last-1)
downOFF
downOFF
to(Last-1)
to(Last-2)
FL-1.5
still_down

## Slide 57: N-Floors elevator
Else
GoF1
s21
s31
….
to1
upON
downOFF
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the elevator must reach the desired floor and then stop – boundary floor
Sp1

## Slide 58: N-Floors elevator
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the elevator must reach the desired floor and then stop – case of an intermediate floor, N in range [2, Last-1]
SpN
Off
GoFN
s1N
s3N
…
toN
upOFF
downOFF
On
upOFF
downOFF
still_up
still_down
still_up
still_down

## Slide 59: N-Floors elevator
Else
GoFLast
s1Last
s2Last
….
toLast
upOFF
downON
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the elevator must reach the desired floor and then stop – boundary floor
SpLast

## Slide 60: N-Floors elevator
FOURTH STEP: SPECIFICATION PHASE
For each button panel command the motor must start and stop once
Off
Go
all sxy
downON
upON
upOFF
downOFF
On
SpLast+1
this notation includes all events of the button panel

## Slide 61: N-Floors elevator
Elevator motor can turn on only if the doors are close.
Doors
Closed
Open
open
close
upON
downON
FOURTH STEP: SPECIFICATION PHASE

## Slide 62: REALISTIC DOOR MODEL
ELEVATOR MODEL’S EXTENSION #2:

## Slide 63: Realistic door model
Before:
Manually moved door
modeled only a sensor able to recognize the door’s position.
Realistic model:
Automatic door, the behavior is controllable
Elevator door closing stops in case of obstruction

## Slide 64: Realistic door model
SENSORS:
DOOR POSITION SENSOR:
“Open doors” proximity switch
“Closed doors” proximity switch
OBSTRUCTION SENSOR:
A photocell capable of detecting obstacles in the door’s way
ACTUATORS:
DOOR WINGS’ MOTOR :
This motor is used to open and close the door wings
FIRST & SECOND STEPS: OUTLINE MODULAR SYSTEM COMPONENTS

## Slide 65: Realistic door model
Events are:
: the doors are completely open
: the doors are completely closed
THIRD STEP: MODELING OF THE COMPONENTS
Door
Note that while the doors are closing, until the sensor recognizes the doors fully closed, the current state is ‘Open’. Same can be said about ‘Closed’ while opening.
fullyopen
Closed
Open
fullyopen
fullyclosed
The sensors of the door can be modeled with a 2-state automaton.
The transitions will be triggered by the proximity sensors of the cabin doors.

## Slide 66: Realistic door model
THIRD STEP: MODELING OF THE COMPONENTS
The sensors of the door can be modeled with a 2-state automaton.
The transitions will be triggered by the proximity sensors of the cabin doors.
Door
fullyopen
Closed
Open
fullyopen
fullyclosed
necessary in case an object is detected while closing, to allow the complete opening of the doors

## Slide 67: Realistic door model
The obstruction sensor is modeled using two states and two events.
objectIN : the sensor signals when the photocell changes its state from free to obstructed
objectOUT : in this case the event represents the photocell going from obstructed to free
Obstruction sensor
Free
Obstr
objectIN
objectOUT
THIRD STEP: MODELING OF THE COMPONENTS

## Slide 68: Realistic door model
THIRD STEP: MODELING OF THE COMPONENTS
Door’s Motor
Closing
Off
closeON
closeOFF
Opening
openON
openOFF
closeToOpen
The motor is modeled through a 3-state automaton, the active condition has been divided in Closing and Opening.
closeOn, openON, closeOFF, openOFF events represent the start or end of an action.
closeToOpen signals a shift in the behaviour, necessary when an obstacle is between the doors.

## Slide 69: Realistic door model
The physical constraints of the system must be fulfilled:
Doors can be fully open only if the motor opened them.
Doors can be fully closed only if the motor closed them.
An object can obstruct the doors if and only if the doors are not shut.
Furthermore, the desired behaviour of the system is the following:
If something is detected between the doors, the doors must be open fully even if the object is immediately removed, for security reasons.
Doors can close only if the photocell state is free.
Movements must be complete: motor is turned off only if the doors are fully open or shut.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 70: Realistic door model
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s start by working on automata of the components.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 71: Realistic door model
THIRD STEP: MODELING OF THE COMPONENTS
Doors can be fully open only if the motor opened them.
Doors can be fully closed only if the motor closed them.
Closing
Off
closeON
closeOFF
Opening
openON
openOFF
closeToOpen
fullyclosed
fullyopen
Door’s Motor (DMot)

## Slide 72: Realistic door model
An object can obstruct the doors only if the doors are not shut
THIRD STEP: MODELING OF THE COMPONENTS
Constraint (Con)
Shut
NotShut
openON
fullyclosed
objectIN
closeToOpen
closeToOpen

## Slide 73: Realistic door model
Doors can close only if no object is between them
THIRD STEP: MODELING OF THE COMPONENTS
Obstruction sensor (Ob)
Free
Obstr
objectIN
objectOUT
fullyclosed

## Slide 74: Realistic door model
There must be a 1 to 1 correspondence of fullyopen signal with an opening command. Fullyopen cannot repeat independently.
THIRD STEP: MODELING OF THE COMPONENTS
Constraint(Con2)
NotOpen
Open
openON
closeToOpen
fullyopen

## Slide 75: Realistic door model
FOURTH STEP: SPECIFICATION PHASE
Doors can close only if the photocell state is free.
closeON
closeOFF
Obstruction sensor (Spda1)
Free
Obstr
objectIN
objectOUT

## Slide 76: Realistic door model
FOURTH STEP: SPECIFICATION PHASE
If something is detected between the doors, the motor cannot turn off before opening the door
OpenAfterObj (Spda2)
0
1
closeON
fullyclosed
2
objectIN
closeToOpen
fullyclosed
objectIN
objectIN
closeOFF

## Slide 77: Realistic door model
FOURTH STEP: SPECIFICATION PHASE
If something is detected between the doors, the motor cannot turn off before opening the door
OpenAfterObj (Spda2)
0
1
closeON
fullyclosed
2
objectIN
closeToOpen
fullyclosed
objectIN
objectIN
closeOFF
fullyclosed represents the limit case of a thin object sliding between the doors right before they close completely

## Slide 78: Realistic door model
FOURTH STEP: SPECIFICATION PHASE
Movements must be complete:
Opening is turned off only after the doors are fully open, then the closing can start
Same with closing
Closed
Open
fullyopen
fullyclosed
Door (Spda3)
fullyopen
closeOFF
openON
openOFF
closeON

## Slide 79: Realistic door model
FOURTH STEP: SPECIFICATION PHASE
After each time the doors are fully open the motor has to stop.
Sp0
Sp1
fullyopen
Spda4
openOFF

## Slide 80: Realistic door model
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s analyze the synchronous compositions.
INDENTIFY CONSTRAINTS AND SPECIFICATIONS:

## Slide 81: Realistic door model
DoorSensor || ObstructionSensor
Physical constraint
Doors can close only if no object is between them
Open-Obstr
Closed-Free
Closed-Obstr
fullyopen
fullyclosed
Open-Free
fullyopen
fullyclosed
objectIN
objectOUT
objectIN
objectOUT
fullyopen
fullyopen

## Slide 82: Realistic door model
PhCd1 DoorSensor || ObstructionSensor
Refined automaton:
Open-Obstr
Closed-Free
Closed-Obstr
fullyopen
fullyclosed
Open-Free
fullyopen
objectIN
objectOUT
objectIN
objectOUT
fullyopen
fullyopen

## Slide 83: Realistic door model
Opening-Open
openON
openOFF
closeToOpen
Closing-Closed
Off-Closed
closeON
closeOFF
Closing-Open
fullyopen
fullyclosed
Off-Open
closeOFF
closeON
fullyopen
fullyclosed
fullyopen
fullyopen
Opening-Closed
fullyopen
fullyopen
fullyclosed
closeToOpen
openON
openOFF
DoorSensor || DoorMotor
Physical constraint

## Slide 84: Realistic door model
Opening-Open
openON
openOFF
closeToOpen
Closing-Closed
Off-Closed
closeON
closeOFF
Closing-Open
fullyopen
fullyclosed
Off-Open
closeOFF
closeON
Opening-Closed
closeToOpen
openON
openOFF
PhCd2 DoorSensor || DoorMotor
Refined automaton:

## Slide 85: Realistic door model
Opening-Open
openON
openOFF
closeToOpen
Closing-Closed
Off-Closed
closeON
closeOFF
Closing-Open
fullyopen
fullyclosed
Off-Open
closeOFF
closeON
fullyopen
fullyclosed
fullyopen
fullyopen
Opening-Closed
fullyopen
fullyopen
fullyclosed
closeToOpen
openON
openOFF
DoorSensor || DoorMotor
Unwanted behaviour

## Slide 86: Realistic door model
Opening-Open
openOFF
closeToOpen
Closing-Closed
Off-Closed
Closing-Open
fullyopen
fullyclosed
Off-Open
closeOFF
closeON
fullyopen
fullyclosed
fullyopen
fullyopen
Opening-Closed
fullyopen
fullyopen
fullyclosed
openON
Spd2 DoorSensor || DoorMotor
Refined automaton:

## Slide 87: Realistic door model
Opening-Open
openOFF
closeToOpen
Closing-Closed
Off-Closed
closeOFF
Closing-Open
fullyclosed
Off-Open
closeON
Opening-Closed
fullyopen
openON
Phcd2 || Spd2
Opening
fullyopen
State added to ensure that openOFF is executed after fullyopen

## Slide 88: Realistic door model
Opening-Obstr
openON
openOFF
closeToOpen
Closing-Free
Off-Free
closeON
closeOFF
Closing-Obstr
objectOUT
Off-Obstr
closeOFF
closeON
objectIN
Opening-Free
objectIN
objectOUT
closeToOpen
openON
openOFF
ObstructionSensor || DoorMotor
Unwanted behaviour
objectIN
objectOUT

## Slide 89: Realistic door model
Spd3
Opening-Obstr
openOFF
closeToOpen
Closing-Free
Off-Free
closeON
Closing-Obstr
Off-Obstr
closeOFF
objectIN
Opening-Free
objectIN
objectOUT
openON
openOFF
objectIN
objectOUT
Closing
objectOUT
objectIN
closeToOpen

## Slide 90: Realistic door model
Spd3
Opening-Obstr
openOFF
closeToOpen
Closing-Free
Off-Free
closeON
Closing-Obstr
Off-Obstr
closeOFF
objectIN
Opening-Free
objectIN
objectOUT
openON
openOFF
objectIN
objectOUT
Closing
objectOUT
objectIN
closeToOpen
State added to memorize the transit of an object in the current closing operation

## Slide 91: Realistic door model
PhCd1||PhCd2||Spd2||Spd3
0
1
2
3
openON
objectIN
objectOUT
closeToOpen
4
5
8
11
6
9
12
7
10
13
fullyopen
fullyopen
openOFF
objectOUT
objectOUT
objectOUT
objectIN
objectIN
objectIN
openOFF
fullyopen
closeON
fullyclosed
closeOFF
objectIN
objectIN
objectOUT
fullyclosed
closeToOpen
closeToOpen
fullyopen
objectIN
objectOUT
objectIN
objectOUT
objectIN
objectOUT

## Slide 92: Realistic door model
In the automaton obtained from the syncronous composition of PhCd1||Spd1||Spd2 are present unfeasible behaviours.
They result from the interaction between the three modules, therefore cannot be prevented acting only on the syncronous composition between pairs of modules.
Unfeasible behaviour: object detected between the doors when they are fully closed (equal to Con)

## Slide 93: Realistic door model
0
1
2
3
openON
objectIN
objectOUT
closeToOpen
4
5
8
11
6
9
12
7
10
13
fullyopen
fullyopen
openOFF
objectOUT
objectOUT
objectOUT
objectIN
objectIN
objectIN
openOFF
fullyopen
closeON
fullyclosed
closeOFF
objectIN
objectIN
objectOUT
fullyclosed
closeToOpen
closeToOpen
fullyopen
DoorAut = PhCd1||PhCd2||Spd2||Spd3||Con
= DSens||DMot||Ob||Con||Con2||Spda1||Spda2||Spda3||Spda4

## Slide 94: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Doors can open only if the elevator motor is off.
Elevator motor can turn on only if the doors are shut.
Elevator motor can turn on only if the door motor is off.
The model of the realistic door must be integrated with the elevator motor and the floor sensor.

## Slide 95: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s start by working on automata of the components.

## Slide 96: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Doors can open only if the elevator motor is off.
Elevator motor Spint1
Down
Off
downON
downOFF
Up
upON
upOFF
to1
to2
openON
fullyopen

## Slide 97: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Elevator motor can turn on only the door motor is off.
Door motor (Spint2)
objectOUT
Closing
Off
closeON
closeOFF
Opening
openON
openOFF
closeToOpen
objectOUT
fullyclosed
fullyopen
upON
downON

## Slide 98: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Elevator motor can turn on only if the doors are shut.
Closed
Open
fullyopen
fullyclosed
Door (Spint3)
fullyopen
closeOFF
openOFF
closeON
upON
downON

## Slide 99: Realistic door model
INDENTIFY SPECIFICATIONS of INTEGRATED CASE:
Similarly to before, two main approaches are possible.
Working directly on automata modeling single components
Working on the synchronous composition: possibly the synchronous composition among a few models
Let’s analyze the synchronous compositions.

## Slide 100: Realistic door model
DoorMotor || ElevatorMotor
Off-Off
Opening-Off
Opening-Down
Off-Down
Closing-Down
Closing-Off
Closing-Up
Off-Up
Opening-Up
closeOFF
closeOFF
closeOFF
closeON
closeON
closeON
openOFF
openOFF
openOFF
openON
openON
openON
downON
downON
downON
downOFF
downOFF
downOFF
upON
upON
upON
upOFF
upOFF
upOFF
Unwanted behaviour
closeToOpen

## Slide 101: Realistic door model
Spi1 DoorMotor || ElevatorMotor
Off-Off
Opening-Off
Off-Down
Closing-Off
Off-Up
closeOFF
closeON
openOFF
openON
downON
downOFF
upON
upOFF
Refined automaton :
closeToOpen

## Slide 102: Realistic door model
DoorPosition || ElevatorMotor
Unwanted behaviour
Open-Off
Open-Up
Open-Down
Closed-Down
Closed-Off
Closed-Up
upON
upON
upOFF
upOFF
downOFF
downON
downOFF
downON
fullyopen
fullyopen
fullyopen
fullyclosed
fullyclosed
fullyclosed
fullyopen
fullyopen
fullyopen

## Slide 103: Realistic door model
Spi2 DoorPosition || ElevatorMotor
Open-Off
Closed-Down
Closed-Off
Closed-Up
upON
upOFF
downOFF
downON
fullyopen
fullyclosed
fullyopen
Refined automaton :

## Slide 104: Realistic door model
Spi1||Spi2||DoorAut||SP1 = Spint1 ||Spint2 ||Spint3 ||DoorAut||Position2||Spb2
F1 - Closed - Off
F1 - Closed - Down
F1 - Closed - Up
downOFF
to2
F2 - Closed - Up
F2 - Closed - Off
upOFF
F2 - Closed - Down
to1
Automatic Door
Automatic Door
openON
closeOFF
upON
downON
openON
closeOFF
The state is a representation of the behaviour showed in slide 93
FINAL RESULT